Interactive Idiots Guide to Tait Base Station System ‘S’ Numbers – (V3a)

S A B C – D E F G – H I J K - L M N O

S									S

A	=	Base Type

B	=	System Type

C	=	PMU Type

D	=	Power Amp Ch 1

E	=	Power Amp Ch 2

F	=	PA Ch 1 Band

G	=	Reciter Ch 1 Sub-Band			
H	=	PA Ch 2 Band				
I	=	Reciter Ch 2 Sub-Band

J	=	SIF Ch 1

K	=	SIF Ch2

L	=	Front Panel Branding

M	=	Power Chord Type

N	=	N/A

O	=	Control Panel Type

Note: 	When a drop down box is selected above, look in the status bar at the bottom of the MS Word window (or press F1) to see any hints for that particular field

# Text boxes

Example for fields ‘F’ and ‘G’:

If  PA Ch 1 Band ‘H=UHF 380-520Mhz’ is selected

Then the only valid Reciter Ch 1 Sub-band choices that can be selected are:

1=(H)UHF 400-440Mhz

2=(H)UHF 440-480Mhz

3=(H)UHF 470-520Mhz

4=(H)UHF 380-420Mhz

Example for fields ‘H’ and ‘I’:

If  PA Ch 2 Band ‘B=VHF 136-174Mhz’ is selected

Then the only valid Reciter Ch 2 Sub-band choices that can be selected are:

1=(B)VHF 136-156Mhz

2=(B)VHF 148-174Mhz